## Slide 1
RESEARCH PROJECT
scCO₂ Pressure
Control System
Automated Control Software — Implementation Plan
Taub Research Group | University of Michigan MSE | March 2026

## Slide 2
scCO₂ Pressure Control System
The Problem
No Rate Control
Pressurization rates vary unpredictably with manual valve adjustment — irreproducible experiments.
Operator Dependent
Results change based on who runs the experiment and how attentive they are at any given moment.
No Data Logging
Pressure vs. time data must be recorded manually — error-prone, incomplete, hard to reproduce.
Safety Risk
No automated overpressure protection or controlled emergency depressurization procedure.
Research Requirement: Constant, reproducible rates — 350 kPa/min pressurize / 2 MPa/min depressurize

## Slide 3
scCO₂ Pressure Control System
Proposed Software Solution
PHASE 1
Simulink Digital Twin
Build a validated physics model of the CO₂ vessel in MATLAB Simulink + Simscape. Use the interactive PID Tuner to find optimal control gains before hardware arrives. No hardware needed — validate everything in software first.
PHASE 2
Python Control Application
Full runtime control system running on Raspberry Pi — deployed when hardware arrives. Simulation mode on Windows for development and testing right now. One line of code to switch from simulation to real hardware.
Cost: ~$0 (open source Python + free MATLAB license)
Timeline: 4 – 6 weeks (parallel with hardware procurement)

## Slide 4
scCO₂ Pressure Control System
System Architecture
PRESSURIZATION PATH
CO₂
Cylinder
5.9 MPa
▶
Victor
Regulator
5.5 MPa
▶
Air-Driven
Booster
28 MPa max
▶
Motorized
Needle Valve
(NEW)
▶
Check
Valve
▶
Pressure
Vessel
28 MPa
DEPRESSURIZATION PATH
Pressure
Vessel
◀
PWM Vent
Solenoid
(NEW)
◀
Manual
Needle Valve
(flow limiter)
◀
Vent to
Fume Hood
CONTROL LOOP
Pressure
Transducer
4-20mA
◀
Raspberry Pi
Controller
(PID)
◀
Stepper Motor
Motorized Valve
(pressurize)
◀
PWM Solenoid
(depressurize)
Hardware Abstraction Layer: same code runs in Windows simulation or on real Raspberry Pi hardware

## Slide 5
scCO₂ Pressure Control System
Phase 1: Simulink Digital Twin
Purpose: Validate control algorithm and tune PID gains before hardware arrives — no risk, no cost
1
Simscape Gas & Thermal Library
Pre-built CO₂ flow blocks — no need to derive equations manually. Connect components like a P&ID diagram.
2
Non-Linear Booster Model
Flow ∝ valve_opening × √(Pₙₒₒₜₒᵉ − Pᵥᵉₛₛᵉℓ). As vessel fills, driving pressure shrinks — PID must compensate.
3
Temperature–Pressure Coupling
Compression heating during pressurization + Joule-Thomson cooling during venting. Both modeled realistically.
4
Interactive PID Tuner
Drag a slider, watch the 350 kPa/min pressure ramp respond in real time. Find optimal Kp, Ki, Kd visually.
Output → Validated Kp, Ki, Kd gains saved and transferred directly to Python deployment

## Slide 6
scCO₂ Pressure Control System
Key Physics: Temperature–Pressure Coupling
1
Compression Heating (Pressurizing)
CO₂ flowing into the vessel compresses and heats up (adiabatic compression). • Temperature spike → additional pressure rise: ΔP/ΔT ≈ 0.084 MPa/°C at operating point. • A 2°C spike → +0.17 MPa extra pressure on top of flow-driven rise. • PID must be tuned carefully to avoid overcorrecting and oscillating.
2
INKBIRD Temperature Controller Lag
INKBIRD PID maintains vessel at 60°C setpoint but has ~15 second response lag. • During rapid pressurization, vessel temperature temporarily overshoots 60°C. • This transient causes pressure to rise faster than the flow-driven model predicts. • Simulation models INKBIRD as a lagged PI controller for realistic behavior.
3
Joule-Thomson Cooling (Venting)
CO₂ expanding through the vent valve cools significantly (Joule-Thomson effect). • Temperature drop → additional pressure drop beyond the vented mass alone. • Creates coupled depressurization behavior — 2 MPa/min rate harder to hold. • Depressurization PID duty cycle must compensate for this coupled cooling.
Pre-condition check: START button is disabled until vessel temperature ≥ 55°C (CO₂ must be supercritical before pressurization)

## Slide 7
scCO₂ Pressure Control System
Phase 2: Python Control Application
SOFTWARE MODULES
config.py
All constants: pressures, rates, PID gains, GPIO pins
hardware/
Simulated (Windows) OR Real RPi hardware — swap one line
control/
PID controller, ramp generator, state machine
logger.py
CSV logging: timestamp, pressure, temp, state, valve %
cloud.py
ThingSpeak upload every 2 sec — monitor from anywhere
gui.py
Tkinter GUI with live pressure & temperature chart
STATE MACHINE
IDLE
▼
PRESSURIZE
350 kPa/min
▼
HOLD
±1–2%
▼
DEPRESSURIZE
2 MPa/min
E-STOP: cuts all outputs instantly from any state

## Slide 8
scCO₂ Pressure Control System
Control Interface
scCO₂ Pressure Control System ● PRESSURIZING
[ Live Chart: Pressure (MPa) vs Time ]
Measured Pressure (MPa)
Setpoint Ramp
PRESSURE
23.85 MPa
RATE
352 kPa/min
TEMPERATURE
61.2 °C
VALVE
67% open
START
HOLD
DEPRESSURIZE
⛔ E-STOP
START disabled until vessel temperature ≥ 55°C

## Slide 9
scCO₂ Pressure Control System
Remote Monitoring — Free Cloud Dashboard
ThingSpeak by MathWorks — Free Tier: 3 Million Messages/Year — No hardware modifications required
WHAT YOU SEE FROM ANYWHERE
Live pressure and temperature charts
Current experiment state (IDLE / PRESSURIZING / HOLDING / DEPRESSURIZING)
Email alert: "Experiment complete" when IDLE state reached
Email alert: "Pressure exceeded limit" if safety threshold hit
Full data history — download CSV directly from dashboard
MATLAB INTEGRATION
Data flows directly from the experiment into MATLAB thingSpeakRead() pulls all channels by experiment ID — no CSV export, no manual steps. Analyze pressure ramp accuracy, temperature correlation, and PID performance directly in MATLAB.
ONE-TIME SETUP
Create free account at thingspeak.com → get API key → paste into config.py
5 minutes. No credit card. Works in simulation mode on Windows too.
$0 cost • No hardware changes • Works from any device, anywhere

## Slide 10
scCO₂ Pressure Control System
Implementation Timeline
Software development proceeds in parallel with hardware procurement — no blocking dependencies.
Weeks 1–2
Phase 1: Simulink Digital Twin
Build Simscape plant model (CO₂ vessel, valve, thermal) • Tune PID using Simulink PID Tuner • Validate 350 kPa/min ramp and 2 MPa/min depress rates • Export Kp, Ki, Kd to configuration file
Weeks 3–4
Phase 2: Python App Development
Build hardware abstraction layer (sim + RPi) • Implement PID, state machine, ramp generator • Develop Tkinter GUI with live pressure/temperature chart • Add CSV logging and ThingSpeak cloud upload
Week 5
Integration & Testing (Windows Simulation)
Full end-to-end test in simulation mode • Verify all safety interlocks (E-stop, watchdog, limits) • Validate cloud monitoring and data logging • Document setup and operating procedures
On Hardware Arrival
RPi Deployment & CO₂ Testing
Wire RPiHardware module to real sensors and actuators • Initial low-pressure N₂ wiring test • CO₂ tests: verify ramp accuracy, fine-tune PID • Full 28 MPa validation run

## Slide 11
Next Steps
1
Create free ThingSpeak account at thingspeak.com and get API key (5 minutes)
2
Confirm MATLAB Simscape Gas/Thermal toolbox is installed (UMich license)
3
Begin Simulink model build — Phase 1 (Weeks 1–2)
4
Order hardware: motorized valve, HP solenoid, pressure transducer (see BOM)
5
Develop Python app in simulation mode on Windows in parallel (Weeks 3–4)
Questions?
Taub Research Group | University of Michigan MSE | March 2026